# ESP32 DEVKITC Pinout

### Inputs/ External Interrupts
SENS_INT_BPM, SENS_INT_SPO2, SENS_INT_ECG done
DISP_INT_TOUCH done

### Outputs
~SENS_RST_ECG, ~SENS_RST_BPM, ~SENS_RST_SPO2, SENS_START done
~SENS_CS_ECG, ~SENS_CS_BPM,~SENS_CS_SPO2 done
DISP_CS_DISP, DISP_CS_TOUCH done

### Display BUS on VSPI (speed optimized)
DISP_MOSI, DISP_MISO, DISP_SCLK done

### Debug
JTAG_~TRST, JTAG_TMS, JTAG_TDI, JTAG_TDO, PROC_SDA, PROC_SCL done

### PROC
PROC_SDA, PROC_SCL done

GPIO	Input	Output	Notes	Function	Comments
0	pulled up	OK	outputs PWM signal at boot, is pulled high
1	TX pin	OK	debug output at boot
2	OK	OK	connected to on-board LED	~SENS_CS_ECG
3	OK	RX pin	HIGH at boot	DISP_CS_TOUCH	Problematic when receiving usart data
4	OK	OK		~SENS_CS_SPO2
5	OK	OK	outputs PWM signal at boot	DISP_CS_DISP
6	x	x	connected to the integrated SPI flash
7	x	x	connected to the integrated SPI flash
8	x	x	connected to the integrated SPI flash
9	x	x	connected to the integrated SPI flash
10	x	x	connected to the integrated SPI flash
11	x	x	connected to the integrated SPI flash
12	OK	OK	boot fail if pulled high	JTAG_TDI	programming; preset;
13	OK	OK		JTAG_TDO	programming; preset;
14	OK	OK	outputs PWM signal at boot	JTAG_TMS	programming; preset;
15	OK	OK	outputs PWM signal at boot	~SENS_CS_BPM
16	OK	OK		PROC_SCL
17	OK	OK		PROC_SDA
18	OK	OK		DISP_SCLK	VSPI Speed optimized
19	OK	OK		DISP_MISO	VSPI Speed optimized
21	OK	OK		~SENS_RST_BPM
22	OK	OK		~SENS_RST_SPO2
23	OK	OK		DISP_MOSI	VSPI Speed optimized
25	OK	OK		SENS_MOSI	HSPI remapped
26	OK	OK		SENS_MISO	HSPI remapped
27	OK	OK		SENS_SCLK	HSPI remapped
32	OK	OK		SENS_START
33	OK	OK		~SENS_RST_ECG
34	OK		input only	SENS_INT_ECG	Input only compatible
35	OK		input only	DISP_INT_TOUCH	Input only compatible
36	OK		input only; SENSOR_VP	SENS_INT_BPM	Input only compatible
39	OK		input only; SENSOR_VN	SENS_INT_SPO2	Input only compatible
EN				JTAG_~TRST	programming; preset;
3V3				SENS_3V3_DIG
EXT_5V				5V_in
GND1,2,3				GND

- HSPI was remapped because of conflict with JTAG

- wrover devkitc (onboard jtag via usb) has different pinout, is more expensive

convert table to text with | as seperator to paste into github