# ESP32 DEVKITC Pinout

### Inputs/ External Interrupts
SENS_INT_BPM, SENS_INT_SPO2, SENS_INT_ECG
DISP_INT_TOUCH

### Outputs
~SENS_RST_ECG, ~SENS_RST_BPM, ~SENS_RST_SPO2
~SENS_CS_ECG, ~SENS_CS_BPM,~SENS_CS_SPO2
DISP_CS_DISP, DISP_CS_TOUCH

### Display BUS on VSPI (speed optimized)
DISP_MOSI, DISP_MISO, DISP_SCLK

### Debug
JTAG_~TRST, JTAG_TMS, JTAG_TCK, JTAG_TDI, JTAG_TDO

### PROC
PROC_SDA, PROC_SCL

## External GPIOs via I2C GPIO Expander
SENS_START, EXPGPIO1, EXPGPIO2, EXPGPIO3, EXPGPIO4, EXPGPIO5, EXPGPIO6, EXPGPIO7

|GPIO|Input|Output|Notes|Function|
|---|---|---|---|---|
|0|pulled up|OK|outputs PWM signal at boot, is pulled high|~SENS_CS_BPM|
|1|TX pin|OK|debug output at boot ||
|2|OK|OK|Needs to be floating while being flashed; |~SENS_CS_ECG|
|3|OK|RX pin|HIGH at boot |DISP_CS_TOUCH|
|4|OK|OK||~SENS_CS_SPO2|
|5|OK|OK|outputs PWM signal at boot,VSPI_CS |DISP_CS_DISP|
|6|x|x|connected to the integrated SPI flash||
|7|x|x|connected to the integrated SPI flash||
|8|x|x|connected to the integrated SPI flash||
|9|x|x|connected to the integrated SPI flash||
|10|x|x|connected to the integrated SPI flash||
|11|x|x|connected to the integrated SPI flash||
|12|OK|OK|boot fail if pulled high;MTDI,HSPI_MISO|JTAG_TDI|
|13|OK|OK|MTCK, HSPI_MOSI|JTAG_TCK|
|14|OK|OK|outputs PWM signal at boot,MTMS, HSPI_CLK|JTAG_TMS|
|15|OK|OK|outputs PWM signal at boot,MTDO,HSPI_CS|JTAG_TDO|
|16|OK|OK||~SENS_RST_BPM|
|17|OK|OK||~SENS_RST_SPO2|
|18|OK|OK|VSPI_CLK|DISP_SCLK|
|19|OK|OK|VSP_MISO|DISP_MISO|
|21|OK|OK|I2C_SDA|PROC_SDA|
|22|OK|OK|I2C_SCL|PROC_SCL|
|23|OK|OK|VSPI_MOSI|DISP_MOSI|
|25|OK|OK||SENS_MOSI|
|26|OK|OK||SENS_MISO|
|27|OK|OK||SENS_SCLK|
|32|OK|OK||GPIOEXP_INT|
|33|OK|OK||~SENS_RST_ECG|
|34|OK||input only|SENS_INT_ECG|
|35|OK||input only|DISP_INT_TOUCH|
|36|OK||input only; SENSOR_VP|SENS_INT_BPM|
|39|OK||input only; SENSOR_VN|SENS_INT_SPO2|
|EN|||Connected to RTS, DTR reset circuit|JTAG_~TRST|
|3V3|||3.3V|SENS_3V3_DIG|
|EXT_5V||||5V_in|
|GND1,2,3|||GND|GND|

Orange Pins are strapping pins.

convert table to text with | as separator to paste into github