# ESP32 DEVKITC Pinout

### Inputs/ External Interrupts
SENS_INT_BPM, SENS_INT_SPO2, SENS_INT_ECG done
DISP_INT_TOUCH done

### Outputs
~SENS_RST_ECG, ~SENS_RST_BPM, ~SENS_RST_SPO2, SENS_START done
~SENS_CS_ECG, ~SENS_CS_BPM,~SENS_CS_SPO2 done
DISP_CS_DISP, DISP_CS_TOUCH done

### Display BUS on VSPI (speed optimized)
DISP_MOSI, DISP_MISO, DISP_SCLK done

### Debug
JTAG_~TRST, JTAG_TMS, JTAG_TDI, JTAG_TDO, PROC_SDA, PROC_SCL done

### PROC
PROC_SDA, PROC_SCL done

- HSPI was remapped because of conflict with JTAG

- wrover devkitc (onboard jtag via usb) has different pinout, is more expensive

convert table to text with | as seperator to paste into github

GPIO	Input	Output	Notes	Function
---	---	---	---	---
0	pulled up	OK	outputs PWM signal at boot, is pulled high
1	TX pin	OK	debug output at boot	~SENS_CS_BPM
2	OK	OK	Needs to be floating while being flashed;	~SENS_CS_ECG
3	OK	RX pin	HIGH at boot	DISP_CS_TOUCH
4	OK	OK		~SENS_CS_SPO2
5	OK	OK	outputs PWM signal at boot,VSPI_CS	DISP_CS_DISP
6	x	x	connected to the integrated SPI flash
7	x	x	connected to the integrated SPI flash
8	x	x	connected to the integrated SPI flash
9	x	x	connected to the integrated SPI flash
10	x	x	connected to the integrated SPI flash
11	x	x	connected to the integrated SPI flash
12MTDI	OK	OK	boot fail if pulled high;HSPI_MISO	JTAG_TDI
13	OK	OK	HSPI_MOSI	JTAG_TDO
14	OK	OK	outputs PWM signal at boot,HSPI_CLK	JTAG_TMS
15MTDO	OK	OK	outputs PWM signal at boot,HSPI_CS
16	OK	OK		PROC_SCL
17	OK	OK		PROC_SDA
18	OK	OK	VSPI_CLK	DISP_SCLK
19	OK	OK	VSP_MISO	DISP_MISO
21	OK	OK		~SENS_RST_BPM~SENS_CS_BPM
22	OK	OK		~SENS_RST_SPO2
23	OK	OK	VSPI_MOSI	DISP_MOSI
25	OK	OK		SENS_MOSI
26	OK	OK		SENS_MISO
27	OK	OK		SENS_SCLK
32	OK	OK		SENS_START
33	OK	OK		~SENS_RST_ECG
34	OK		input only	SENS_INT_ECG
35	OK		input only	DISP_INT_TOUCH
36	OK		input only; SENSOR_VP	SENS_INT_BPM
39	OK		input only; SENSOR_VN	SENS_INT_SPO2
EN			Connected to RTS, DTR reset circuit	JTAG_~TRST
3V3			3.3V	SENS_3V3_DIG
EXT_5V			GND	5V_in
GND1,2,3				GND

jtag tdck missing